1.	Introduction									3

1.1	Purpose of Procurement Guidelines Report					3

1.2	Reporting Period								3

1.3	Balancing Services								4

1.4	Structure of Report								4

1.5	Services not included in the report						5

1.6	Comparison with previous year						5

2.	Services Procured Via Market Arrangements				6

2.1	Reactive Power								6

2.2	Market Arrangements for Reactive Power					6

2.3	Default Arrangements for Reactive Power					7

2.4	Reactive Power Comparison with previous year				8

2.5	Fast Reserve (Contracted)							9

2.6	Fast Reserve (Tendered) Comparison with previous year			10

2.7	Short Term Operating Reserve (STOR) including Balancing

Mechanism (BM) and Non Balancing Mechanism (NBM)			11

2.8	STOR Comparison with previous year					14

2.9	Tendered Frequency Response.						15

3.	Services Procured Via Non-Tendered Bilateral Contracts			15

3.1	Mandatory Frequency Response						15

3.2	Commercial Frequency Response						16

3.3	Frequency Response Comparison with previous year			17

3.4	Fast Start									19

3.5	Black Start									20

3.6	BM Start up									21

3.7	BM Start up Comparison with previous year					21

3.8	Fast Reserve (Procured on a Non-Tendered basis)				22

3.9	Non-tendered Fast Reserve Comparison with previous year		22

3.10	System to System Services							23

3.11	SO-SO Comparison with previous year					24

3.12	System to Generator Operational Inter-tripping Schemes			26

3.13	Commercial Intertrip Service							27

3.14	Balancing Services Contracts to manage System Issues			29

3.15	System Issues Comparison with previous year				31

3.16	Maximum Generation Service						32

3.17	All Other Services								32

4.	Energy Related Products							33

4.1	Forward Trading								33

4.2	Trades Comparison with previous year					34

4.3	Pre-Gate BMU Transactions (PGBT)						36

4.4	PGBTs Comparison with previous year					36

5.	Constraints									37

5.1	BM Constraints Comparison with previous year				37

6.	Summary									38

6.1	Summary Chart								38

6.2	Further information								39

6.3	Contact and Feedback							39

7.	Appendices									40

7.1	Appendix 1									40

7.2	Appendix 2									41

# INTRODUCTION

National Grid procures Balancing Services subject to the framework laid down in Condition C16 of the Transmission Licence. This framework obliges National Grid to “operate the transmission system in an efficient, economic and co-ordinated manner” and also requires a number of statements and reports on the procurement and use of Balancing Services to be established. The Procurement Guidelines is one of these statements, and sets out the principles used in our procurement of Balancing Services, the kinds of Balancing Services that we may be interested in purchasing and the mechanisms by which we do so.  The Procurement Guidelines is published on National Grid’s website and is subject to annual review and industry consultation.  When a new Procurement Guidelines statement is published annually (covering the forthcoming relevant period), National Grid is required to produce a Procurement Guidelines Report (“Report”) covering the preceding relevant period, having previously agreed the ‘form’ of the Report with The Authority.

1.1	Purpose of Procurement Guidelines Report

The purpose of the Report is to provide information in respect of the relevant1 Balancing Services that National Grid has procured in the defined reporting period.

1.2	Reporting Period

In accordance with Condition C16 of the Transmission Licence, the Report will be produced within one month after the date on which each revised Procurement Guidelines Statement is to be published.

The information utilised in this report is the best available at the time of publication and may be subject to minor changes as a result of final reconciliation.

1 Scope of the balancing services covered in this document can be found in section 1.3                 and 1.5

1.3	Balancing Services

The Balancing Services National Grid has procured, either via market arrangements or bilateral contracts, throughout the period covered by the Report, are:

 Frequency Response

 Reactive Power

 Fast Start

 Black Start

 Reserve Services - Fast Reserve, STOR and BM Start-Up

 System to System Services

 Inter-trips

 Ancillary Contracts to manage System issues

 Maximum Generation Service

 All Other Services

 Energy Related Products (including PGBTs)

 BM Constraints

It is important to note that Balancing Services are procured from both Balancing Mechanism and Non Balancing Mechanism Parties.

1.4	Structure of Report

This report presents the Balancing Services under four main titles:-

 Services Procured via Market Arrangements

 Services Procured via Non-Tendered Bilateral Contracts

 Other Energy Related Products

 Constraints

It is then followed by a summary section providing the high level information for all services for the financial year 2014-15.

1.5	Services not included in the report

The scope of the Procurement Guidelines does not include the acceptance of Bids and Offers in the Balancing Mechanism. However, Bids and Offers for Constraint management (see section 5) and BM STOR Utilisation (see section 2.7) have been included to provide an appreciation of the overall costs. Further information on Bid and Offer acceptances can be found in the Balancing Principles Statement Report.

1.6	Comparison with previous year

The total cost of Balancing Services has increased by £22m from £750m in 2013/14 to £772m in 2014/15. Constraint and intertrip costs saw the biggest reduction of £37m in 2014/15. STOR costs also reduced by £28m from £97m in 2013/14. Forward trades however, increased by £85m from -£14m in 2013/14. The reasons behind the changes discussed above are analysed in more detail in the relevant sections of this report.

# Services Procured Via Market Arrangements

2.1	Reactive Power

National Grid manages voltage on the transmission system within statutory limits to ensure quality of supply in line with the National Electricity Transmission System Security and Quality of Supply Standards (NETS SQSS). In doing this we ensure that reactive power resources are provided on a localised basis to meet the constantly varying needs of the system, and that there is sufficient reactive power reserve available to meet contingencies.

2.2	Market Arrangements for Reactive Power

There were two tender rounds (TR33, TR34) covering April 2014 to March 2015 period. No tenders were received for this period. Further information regarding each of these tender rounds can be found at the following website address:

http://www2.nationalgrid.com/UK/Services/Balancing-services/Reactive-power-services/Reactive-Market-Tender/

Utilisation volume of Reactive Power under Market and Default arrangements over the relevant period are detailed in the chart below.

There was no reactive power utilisation volumes under market arrangements as a result of no tenders being received for the period.

2.3	Default Arrangements for Reactive Power

Further information regarding the default payment arrangements can be found at the following National Grid Website.

http://www2.nationalgrid.com/uk/services/balancing-services/reactive-power-services/

2.4	Reactive Power Comparison with previous year

Total Reactive costs have increased by 39.3% from ~£54.35m in 2014/15 to ~£75.7m in 2015/16, while the utilisation increased by 31% from ~22TVARh in 2014/15 to ~29TVARh in 2015/16. The average monthly Reactive Default Price in 2014/15 decreased by 16.8% from £2.99/MVARh in 2015/16 to £2.56/MVARh.

Utilisation volume and costs of Reactive Power under Market and Default arrangements for the last 10 years are detailed in the charts below. The proportion of utilisation under from units under “market arrangement” has been shrinking; and in the previous five years, reactive power was purchased solely via the default arrangement. In some instances additional Balancing Service contracts were taken to ensure generators were running and thus able to provide reactive power via the default mechanism. The costs of these addition contracts are reported in section 3.14.

Further information regarding the default payment arrangements can be found at the following National Grid Website:

http://www2.nationalgrid.com/uk/services/balancing-services/reactive-power-services/

2.5	Fast Reserve

Further information explaining Fast Reserve and the assessment criteria of tenders can be found on the National Grid Website.

http://www2.nationalgrid.com/UK/services/Balancing-services/Reserve-services/Fast-reserve/

2.6 Fast Reserve (Tendered) Comparison with previous year

The following graph shows the monthly variation in nomination hours from the contracted Fast

Reserve Capacity.

The nominated volume of Fast Reserve in 2015/16 has reduced to 1,429GWh, from 1,831GWh in 2014/15. This was due to National Grid optimising the contracted Fast Reserve position from October 2014, through reducing the contracted requirement from 400MW to 300MW. Additionally, slightly lower prices for contracted Fast Reserve were seen in 2014/15 leading to a 14% reduction in costs from £16m in 2013/14 to £13.7 in 2014/15.

2.7	Short Term Operating Reserve (STOR) including Balancing Mechanism (BM) and Non Balancing Mechanism (NBM)

National Grid procures Short Term Operating Reserve (STOR) through a competitive tender process which is conducted three times per year.

Further information on STOR can be found on the National Grid website.

http://www2.nationalgrid.com/uk/services/balancing-services/reserve-services/short-term-operating-reserve/

The increase and fall in the proportion of STOR NBM Committed and Flexible utilisation during 2015/16 is seasonally driven by the NBM market’s provision of Committed and Flexible STOR services. During the winter seasons (November to March) a large proportion of the NBM market switches from a committed service to the flexible service. More details can be found in the STOR market reports.

STOR BM and NBM Utilisation Volume and Costs (Data)

| Month | STOR BM Committed Util Cost £m (Settlement) | STOR NBM Committed Util Cost £m | STOR NBM Flexible Util Cost £m | STOR BM Committed Utilisation MWhrs | STOR NBM Committed Utilisation MWhrs (Inc Ramp Energy) | STOR NBM Flexible Utilisation MWhrs (Inc Ramp Energy) |
| --- | --- | --- | --- | --- | --- | --- |
| Apr-15 | 0.196 | 0.335 | 0.210 | 1,232.970 | 4,058.640 | 2,971.460 |
| May-15 | 0.359 | 0.577 | 0.351 | 1,974.670 | 6,780.340 | 4,549.990 |
| Jun-15 | 0.204 | 0.569 | 0.369 | 1,316.250 | 6,283.280 | 5,038.080 |
| Jul-15 | 0.544 | 0.519 | 0.292 | 3,208.616 | 5,610.295 | 4,042.254 |
| Aug-15 | 0.690 | 0.828 | 0.560 | 3,964.897 | 9,330.367 | 7,230.696 |
| Sep-15 | 0.765 | 0.776 | 0.508 | 4,350.283 | 8,750.249 | 6,998.367 |
| Oct-15 | 1.143 | 0.443 | 0.472 | 6,745.825 | 4,888.961 | 6,142.736 |
| Nov-15 | 1.069 | 0.036 | 0.455 | 6,419.459 | 310.018 | 5,813.315 |
| Dec-15 | 0.315 | 0.032 | 0.341 | 1,920.205 | 322.294 | 4,476.482 |
| Jan-16 | 0.934 | 0.059 | 0.978 | 5,584.473 | 622.114 | 11,862.922 |
| Feb-16 | 0.277 | 0.030 | 0.372 | 1,690.583 | 307.932 | 4,646.997 |
| Mar-16 | 0.319 | 0.047 | 0.978 | 1,928.266 | 507.187 | 12,268.047 |

[Please note graphs and the table above do not reflect any seasonal reconciliation due to non-availability]

Non Balancing Mechanism (Non-BM) STOR Availability payments, Non-BM STOR Utilisation payments and BM STOR Availability payments are paid as Ancillary Services. BM STOR Utilisation payments are paid via the BM Bids and Offers, not as an Ancillary Service; they are included in this report to clarify the total STOR expenditure. STOR BM Utilisation costs in this report are based on actual spend (i.e. MWh Utilised x Utilisation Price for that BM STOR unit).

# 2.8	STOR Comparison with previous year

Total STOR costs for 2015/16 were £69m - £19m lower than in 2014/15.  This reduction has occurred in all areas of cost. A large decrease has been seen in BM availability costs, this has been driven by NBM units making up an increased shared of the market at lower prices than previous BM availability prices. Availability prices across all service types have continued to drop along with the associated utilisation prices. The average availability price paid for 2015/16 was £4.71/MW/h compared to £6.29/MW/h for 2014/15.

2.9	Tendered Frequency Response.

Please see Section 3.2 Services Procured via Non-Tendered Bilateral Contracts.

# Services Procured Via Non-Tendered Bilateral Contracts

3.1	Mandatory Frequency Response

Mandatory Frequency Response is a compulsory service provided by large generators (>100MW) to automatically change their active power output in response to a change in system frequency.  The Grid Code Connection Condition 6.3.7 and 8.1 describe the technical requirements for this service.

Payments for Mandatory Frequency Response comprise a Holding Payment (£/MW/h) and a Response Energy Payment (£/MWh).  Details on frequency response holding volumes are given below. More information on this can be found on the National Grid Website.

http://www2.nationalgrid.com/uk/services/balancing-services/frequency-response/mandatory-frequency-response/

The next chart shows the Average Holding price paid for Mandatory Frequency Response.

The methodology for calculating Mandatory Frequency Response energy payments is given in CUSC section 4.1.3.9 & 4.1.3.9A.

http://www2.nationalgrid.com/UK/Industry-information/Electricity-codes/

3.2	Commercial Frequency Response

Commercial Frequency Response is a collection of services that can be provided by demand side participants and generation plant. The technical characteristics of these services are different to those required under mandatory service arrangements, and range from enhanced mandatory dynamic services through to non-dynamic services effected via Low Frequency relays. Part of the contract portfolio includes services provided by demand side participants via the Frequency Control by Demand Management (FCDM) service and through Firm Frequency Response (FFR) tender rounds.

Further information on Commercial Frequency Response is available on the National Grid Website, or specifically on firm frequency response through the tenders and reports section of National Grid’s Balancing Services website.

http://www2.nationalgrid.com/uk/services/balancing-services/frequency-response/

The response holding volume shown in the chart above is the Primary response capability or Secondary response capability if no Primary is offered. The costs are the total cost for all capabilities (Primary, Secondary and High).

3.3	Frequency Response Comparison with previous year

There was a £11m increase in commercial frequency response costs in 15/16, to £127m. This was partly offset by a £16m reduction in Mandatory frequency response costs to £28m. This gives an overall year-on-year decrease of £5.4m, or 3.4%.

A higher volume of commercial frequency response in 15/16 was the main reason for the increase in costs. This has had the effect of displacing a large volume of Mandatory holding volume and potential costs.

3.4	Fast Start

Fast Start is the ability of generation to start rapidly from a standstill condition, either via a Low Frequency triggered relay or through manual instruction; and to deliver its rated power output automatically within a defined time period. The Fast Start service is a legacy service and as such volumes and costs are not expected to change significantly. Utilisation of the Fast start service in 2015/16 was a little lower than 2014/15. Fast Start Capability and Utilisation Costs have come in at £4.2m in 2015/16.  Fast Start costs per month from April 2015 to March 2016 can be found below:

3.5	Black Start

In 2015/16 the number of providers with Black Start agreements in place decreased from 15 stations to 13. Total costs have decreased by 25% from £24m in 2014/15 to £19.2m 2015/16.

[Please note that the above chart and table do not include the costs incurred in warming and running Blackstart units to maintain service availability]

Further information on Black Start can be found on the National Grid Website.

http://www2.nationalgrid.com/uk/services/balancing-services/system-security/black-start/

3.6	BM Start up

The chart below contains information relating to the procurement of BM Start up Balancing Services:

3.7	BM Start up Comparison with previous year

The number of BM Start up instructions issued during 2015/16 was 191 compared to 46 instructions during the previous year.  In terms of costs, £0.87m was spent on this service in 2015/16 compared to £1.1m in 2014/15.

Further details are available via the National Grid Website.

http://www2.nationalgrid.com/uk/services/balancing-services/reserve-services/bm-start-up/

3.8	Fast Reserve (Procured on a Non-Tendered basis)

Non-Tendered Fast Reserve is a service that is contracted on a bilateral basis with service providers.  The nature of the service is similar to the Firm Fast Reserve service although the payment and utilisation mechanisms differ for each service.

3.9	Non-tendered Fast Reserve Comparison with previous year

Non-tendered Fast Reserve costs have increased by 16% from £59m in 2014/15 to £68.81m in 2015/16.

Unit capability fees have also increased from £1.75m to £1.79m in 2015/16.

3.10	System to System Services

System to System services are provided mutually with other Transmission System Operators connected to the GB system via interconnectors. Such services are typically used to manage interconnector transfer profiles and to increase or reduce power flows across an interconnector to resolve transmission constraints on either side, or provide Emergency Assistance if required.

The graph below shows the total net volume imported and exported between Great Britain, France and Ireland. Please see Appendix 1 for further clarification on System Operator to System Operator (SO-SO) services.

For definition see Appendix 1

3.11	SO-SO Comparison with previous year

Total System Operator to System Operator Costs have reduced from £5 million in 2014/15 to £4 million in 2015/16 as shown in the graph below.

The volume of SO-SO trades undertaken decreased this year from 39GWh net in 2014/15 to

30GWh net in 2015/16.

There has been a significant decrease in import volume to the UK from 15GWh in 2014/15 to 15GWh in 2015/16. This represents a move on the part of National Grid away from using SO-SO actions towards other, more economic tools for managing the wider system. Export volumes remained roughly similar at 20GWh per year.

SONI represents actions on both EWIC and Moyle although a limited number of actions were

taken on Moyle due to serious fault which occurred in April 2013, curtailing the capability to 50%.

SO-SO trade services are still not available over the BritNed Interconnector due to contractual

and market differences between the UK and Dutch markets.

3.12	System to Generator Operational Inter-tripping Schemes

As a consequence of their connection conditions, certain generators are obligated to have in place operational intertrip schemes.

These schemes fall under a number of different category types as defined under section 4.2.A of the CUSC which describes the respective compensation arrangements. A proportion of these categories entitle the counterparty to payments for maintaining the capability to provide the intertrip and also following utilisation of the service.

Total costs for System to Generator Operational Inter-tripping Schemes has increased from  £1.14m for reporting year 2014/15 to £1.37m in 2015/16.

3.13	Commercial Intertrip Service

In addition to System to Generator Operational Inter-tripping Schemes, National Grid will seek to, where it proves economic and efficient to do so, enter into Commercial Intertrip schemes to assist with managing system issues.

The total expenditure on Commercial Intertrips has increased from £10m in 2014/15 to £11.02m in 2015/16.

Commercial Intertrip Monthly Summary

| Month | Capability Payment £'s | Arming Payment £'s | Number of Hours of Intertrip Arming, Outside of Pre-Paid Arming Contract(s) | Contracted Pre-paid Arming £'s | Number of Hours Armed under Pre-Paid Arming Contract(s) | Number of Trips | Tripping Payment £'s |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Apr-15 | 126,763 | 1,769,173 | 207 | 0 | 0 | 0 | 0 |
| May-15 | 130,989 | 1,191,104 | 337 | 0 | 0 | 0 | 0 |
| Jun-15 | 126,763 | 365,530 | 140 | 0 | 0 | 0 | 0 |
| Jul-15 | 134,381 | 414,845 | 172 | 0 | 0 | 0 | 0 |
| Aug-15 | 134,381 | 955,125 | 314 | 0 | 0 | 0 | 0 |
| Sep-15 | 129,390 | 108,945 | 51 | 0 | 0 | 0 | 0 |
| Oct-15 | 134,560 | 523,105 | 173 | 0 | 0 | 0 | 0 |
| Nov-15 | 130,219 | 1,358,270 | 463 | 0 | 0 | 0 | 0 |
| Dec-15 | 134,560 | 1,206,330 | 553 | 0 | 0 | 0 | 0 |
| Jan-16 | 134,560 | 879,940 | 305 | 0 | 0 | 0 | 0 |
| Feb-16 | 125,879 | 580,950 | 200 | 0 | 0 | 0 | 0 |
| Mar-16 | 134,560 | 88,290 | 39 | 0 | 0 | 0 | 0 |

Under commercial intertrip agreements arming is payable either as;

1. A fixed pre-agreed sum, this may be for a fixed number of hours or unlimited hours (shown above as Contracted arming) or;

2. Payable on utilisation with the generator typically having the right to alter their payments with a short notice period (shown above as Arming Payments).

3. The “Contracted Pre-Paid Arming” column indicates the maximum firm payment that could be made assuming the intertrip is available for use for all the Contracted Arming hours during the contracted period.

3.14	Balancing Services Contracts to manage System Issues

On occasion, National Grid enters into bespoke Balancing Services contracts to manage certain transmission system issues such as voltage issues or system inertia.  The contracts agreed via tender runs are available on the National Grid website, some of them however, by the nature of these contracts, remain confidential.  The costs reported here include any costs of ‘Transmission Related Agreements’, which are entered as a consequence of certain customer choices of connection conditions.

More information related to contracts designed to economically and effectively manage forecast constraint cost and volumes, arising from declining MVAr demand and low levels of expected generation overnight, can be found on the National Grid Website:

http://www2.nationalgrid.com/UK/Services/Balancing-services/System-security/Transmission-Constraint-Management/Transmission-Constraint-Management-Information/

3.15	System Issues Comparison with previous year

The costs of managing Transmission System constraints via contracts decreased from £53.43m in 2013/14 to £21.06m in 2014/15. Commercial Intertrip costs have also decreased from £14.36m in 2013/14 to £9.89m in 2014/15.

The constraint contract costs is the amount spent on contracts with generators to manage constraint groups as economically as possible and avoid cost that would have otherwise been accrued in the Balancing Mechanism. Costs have decreased since last year and this will be due to the nature of the contracts procured, which is in turn dependant on the outages that were taken in 2014/15. The commercial intertrip costs are the costs of arming generator intertrips to manage constraints, major contributors to this figure have been SCOTEX and SWALEX constraint boundaries.

3.16	Maximum Generation Service

The Maximum Generation Service (MGS) is required to provide additional short term generation output during periods of system stress for energy balancing. This service allows access to unused capacity outside of the Generator’s normal operating range. MGS will be initiated by the issuing of an Emergency Instruction in accordance with the Grid Code BC2.9.2.  Details of the service are contained in the CUSC section 4.2

Further details on the utilisation and availability of the service are available on the National Grid Website.

http://www2.nationalgrid.com/uk/services/balancing-services/system-security/maximum-generation/

This service was not utilised during 2013, 2014 or 2015.

3.17	All Other Services

These include costs relating to trading fees and liabilities which are expected to be paid as a result of contracts awaiting signature or unresolved disputes. In 2014/15 costs have decreased to £0.25m from £1.17m in reporting year 2013/14.

# Energy Related Products

4.1	Forward Trading

National Grid’s forward trading is undertaken to reduce the overall costs of balancing the system, and to resolve system issues as appropriate. There are a number of products and procurement mechanisms available.

4.2	Trades Comparison with previous year

There has been an increase in both non-locational and BMU specific trading over the last financial year reflecting National Grid’s continued efforts to employ the most economic mechanism for energy balancing and system management. The 360GWh increase in non-locational purchases is largely reflective of an increased energy requirement resulting from margin shortfall.  This also reflects a negligible increase in intra-day activity for energy balancing purposes.

The 700GWh increase in BMU specific purchases was driven by a higher number of instances of locational specific system constraints requiring additional synchronous plant. The number of constraints requiring the de-sync of plant reduced, leading to a 450GWh decrease in BMU specific sells. The volume of trades undertaken on IFA and Britned for system management remained broadly constant year-on-year.

Further details are available on the National Grid Website

http://www2.nationalgrid.com/UK/Services/Balancing-services/Trading/

4.3	Pre-Gate BMU Transactions (PGBT)

Information on PGBT activity transactions is given in the chart below:

4.4	PGBTs Comparison with previous year

There were no Pre-Gate BMU Transactions undertaken in 2014/15.

Details on real time PGBT transactions can be found on the BMRS (system warning page) and post event, on the National Grid Website.

http://www.nationalgrid.com/uk/Electricity/Balancing/services/energyrelated/pgbt/

# Constraints

National Grid resolves constraints in the GB Transmission System through different mechanisms, including Bids and Offers in the Balancing Mechanism, PGBTs, Trades and System to System Services (SO-SO). The costs of resolving constraints via intertrip contracts (see section 3.13) and bilateral contracts (see section 3.14) have already been explored.

Information on BM constraints activity for the year is given in the chart below

5.1	BM Constraints Comparison with previous year

BM Constraints Costs for reporting year 2014/15 out turned at £260.4m compared to £270.7m in 2013/14. Significant capital investment schemes have continued to reduce capacity on the network, requiring continued spend to manage constraints. Over running of some large schemes were exacerbated by some significant storms and high wind days increasing the cost of managing Scottish constraints.

# Summary

As a summary of financial activity, the following breakdown of balancing services costs is provided by category, for the financial year 2015/16.

6.1	Summary Chart

The information presented in the chart below is analysed in more detail in the relevant sections of this report.

6.2	Further information

For further information on the types of Balancing Services that National Grid intends to procure, please refer to the prevailing Procurement Guidelines.  Information on bid and offer acceptances in the Balancing Mechanism is contained within the Balancing Principles Statement Report and published via the http://bmreports.com website. These documents, along with the Procurement Guidelines Report, are published in accordance with Standard Condition C16 of the Transmission Licence and are available on National Grid’s website.

# 6.3	Contact and Feedback

National Grid welcomes feedback on any aspect of this report including suggestions for future reports. For any comments please email Electricity Codes at soincentives@nationalgrid.com

# 7.1	Appendix 1: System to System Services Definitions

| Initiator | Definition |
| --- | --- |
| NG buy from RTE | National Grid request to RTE for additional energy to GB |
| NG sell to RTE | National Grid request to RTE for reduced energy to GB |
| RTE sell to NG | RTE request to National Grid for additional energy to GB |
| RTE buy from NG | RTE request to National Grid for reduced energy to GB |
| NG buy from SONI | National Grid request to SONI for additional energy to GB |
| NG sell to SONI | National Grid request to SONI for reduced energy to GB |
| SONI sell to NG | SONI request to National Grid for Additional energy to GB |
| SONI buy from NG | SONI request to National Grid for reduced energy to GB. |

RTE = Reseau de Transport de l'Electricite (French electricity grid operator)

NG = National Grid

SONI = System Operator Northern Ireland

# 7.2	Appendix 2: Table of Raw Data

# Text boxes

March 2016

Procurement Guidelines Report

1 April 2015/16

As required by Standard Condition C16 of the National Grid’s Electricity Transmission Licence.

Error! Not a valid link.